## Slide 1
W
W
,
hat is
oT
Payloads
and
Headers
Notes: Hello! In the Web of Things, there are smart devices exchanging data and such data is sent via protocols. All protocols have different mechanisms to separate the data into headers and payloads. So, it is important to understand the difference and how they are relevant for the Web of Things. Thus, this video we going to talk about payloads, headers, different types of payloads, and the most used one in the Web of Things scope..

## Slide 2
Preliminary tutorials to WoT
W3C WoT standards
Notes: This is an introductory series that presents technologies and standards relevant to the Web of Things. If you want to skip directly to the tutorials on the W3C Web of Things standards, click the link in the video description.
Intro of the all concepts.

## Slide 3: What is a Payload?

## Slide 4
Server
Computer
Smart Phone
Computer
Temperature Sensor
Notes: In computing, the payload is the part of transmitted data that is the actual intended message of the application and nothing to do with the protocol itself.

## Slide 5
Temperature Sensor
Computer
Notes: In computing, the payload is the part of transmitted data that is the actual intended message of the application and nothing to do with the protocol itself.

## Slide 6
Smart Phone
Server
Notes: In computing, the payload is the part of transmitted data that is the actual intended message of the application and nothing to do with the protocol itself.

## Slide 7
Computer
Computer
Notes: In computing, the payload is the part of transmitted data that is the actual intended message of the application and nothing to do with the protocol itself.

## Slide 8
Smart Phone
Server
Notes: In computing, the payload is the part of transmitted data that is the actual intended message of the application and nothing to do with the protocol itself.

## Slide 9
Notes: It is also called the body of the message. It is not mandatory in most protocols.

## Slide 10
Header
Payload
Notes: It is also called the body of the message. It is not mandatory in most protocols.

## Slide 11
Protocol
Notes: We can approach with an analogy, where we consider protocols as a truck. A payload should not tell what it should be done by itself. In that sense, we can think of protocol as a truck

## Slide 12
Protocol
Notes: We can approach with an analogy, where we consider protocols as a truck. A payload should not tell what it should be done by itself. In that sense, we can think of protocol as a truck

## Slide 13
Payloads
Notes: Here, we can think of the parcel contents as the payloads of a protocol.
The parcel contents should not contain any information about their destination, the fact that they are transported with a truck or the color of the truck.
In a protocol, payloads are very similar to parcel contents carried by a truck

## Slide 14
What is a Header?

## Slide 15
Header
Payload
Notes: The header is part of a message that can and should be understood by the protocol stack. All the information that the payload should not contain, goes to the header.

## Slide 16
Notes: Let's continue with the parcel-truck example. In that example, the header would be the etiquette on the parcel.
This is what an HTTP header can look like. A header can contain information like request context, response context, status and it can indicate payload type.

## Slide 17: What a header can contain?
304 Not Modified
Access-Control-Allow-Origin: *
Age: 2318192
Cache-Control: public, max-age=315360000
Connection: keep-alive
Date: Mon, 18 Jul 2016 16:06:00 GMT
Server: Apache
Vary: Accept-Encoding
Notes: Let's continue with the parcel-truck example. In that example, the header would be the etiquette on the parcel.
This is what an HTTP header can look like. A header can contain information like request context, response context, status and it can indicate payload type.

## Slide 18: What a header can contain?
304 Not Modified
Access-Control-Allow-Origin: *
Age: 2318192
Cache-Control: public, max-age=315360000
Connection: keep-alive
Date: Mon, 18 Jul 2016 16:06:00 GMT
Server: Apache
Vary: Accept-Encoding
Notes: Let's continue with the parcel-truck example. In that example, the header would be the etiquette on the parcel.
This is what an HTTP header can look like. A header can contain information like request context, response context, status and it can indicate payload type.

## Slide 19: What a header can contain?
304 Not Modified
Access-Control-Allow-Origin: *
Age: 2318192
Cache-Control: public, max-age=315360000
Connection: keep-alive
Date: Mon, 18 Jul 2016 16:06:00 GMT
Server: Apache
Vary: Accept-Encoding
Notes: Let's continue with the parcel-truck example. In that example, the header would be the etiquette on the parcel.
This is what an HTTP header can look like. A header can contain information like request context, response context, status and it can indicate payload type.

## Slide 20
Different Payload Types
Notes: There are different payload types: JSON, XML, CBOR, Text, Audio…

## Slide 21
Different Payload Types
JSON
Notes: There are different payload types: JSON, XML, CBOR, Text, Audio…

## Slide 22
Different Payload Types
XML
Notes: There are different payload types: JSON, XML, CBOR, Text, Audio…

## Slide 23
Different Payload Types
CBOR
Notes: There are different payload types: JSON, XML, CBOR, Text, Audio…

## Slide 24
Different Payload Types
Text
Notes: There are different payload types: JSON, XML, CBOR, Text, Audio…

## Slide 25
Different Payload Types
Audio, video etc.
Notes: There are different payload types: JSON, XML, CBOR, Text, Audio…

## Slide 26
Different Payload Types
JSON
XML
CBOR
Text
Audio, video etc.
Notes: There are different payload types: JSON, XML, CBOR, Text, Audio…

## Slide 27: JSON Examples
Notes: So let us show you an example of JSON payload. This is a temperature payload, a single number. And this is a configuration payload. It is a JSON object consisting of key/ value pairs desiredUnit and updateInterval. The temperature payload is sent from the sensor and the configuration is sent to the sensor.

## Slide 28: JSON Examples
90
Temperature
payload
Notes: So let us show you an example of JSON payload. This is a temperature payload, a single number. And this is a configuration payload. It is a JSON object consisting of key/ value pairs desiredUnit and updateInterval. The temperature payload is sent from the sensor and the configuration is sent to the sensor.

## Slide 29: JSON Examples
{
"desiredUnit":"celcius",
"updateInterval":30,
}
Configuration
payload
90
Temperature
payload
Notes: So let us show you an example of JSON payload. This is a temperature payload, a single number. And this is a configuration payload. It is a JSON object consisting of key/ value pairs desiredUnit and updateInterval. The temperature payload is sent from the sensor and the configuration is sent to the sensor.

## Slide 30: JSON Examples
{
"desiredUnit":"celcius",
"updateInterval":30,
}
Configuration
payload
90
Temperature
payload
Temperature
Sensor
Notes: So let us show you an example of JSON payload. This is a temperature payload, a single number. And this is a configuration payload. It is a JSON object consisting of key/ value pairs desiredUnit and updateInterval. The temperature payload is sent from the sensor and the configuration is sent to the sensor.

## Slide 31: JSON Examples
Temperature
Sensor
90
Temperature
payload
{
"desiredUnit":"celcius",
"updateInterval":30,
}
Configuration
payload
Notes: So let us show you an example of JSON payload. This is a temperature payload, a single number. And this is a configuration payload. It is a JSON object consisting of key/ value pairs desiredUnit and updateInterval. The temperature payload is sent from the sensor and the configuration is sent to the sensor.

## Slide 32: JSON Examples
{
"desiredUnit":"celcius",
"updateInterval":30,
}
90
Temperature payload
Configuration payload
Temperature Sensor
Notes: So let us show you an example of JSON payload. This is a temperature payload, a single number. And this is a configuration payload. It is a JSON object consisting of key/ value pairs desiredUnit and updateInterval. The temperature payload is sent from the sensor and the configuration is sent to the sensor.

## Slide 33
Why is JSON important?
Notes: In the next video series, we will talk in detail, about JSON. But first let us explain why is JSON so important?

## Slide 34
Configuration
Files
TD
TM
JSON
Notes: Because JSON is very relevant in the scope of the Web of Things, payloads are preferred mostly in JSON. Also, many other API and configuration files use JSON.

## Slide 35
XML
CBOR
<root>
<element>
<isActive>true</isActive>
<lastCalibration>2018-11-13</lastCalibration>
<measurement>
<unit>Celsius</unit>
<value>25</value>
</measurement>
<precision>0.1</precision>
<type>Temperature Sensor</type>
</element>
<element>
<isActive>true</isActive>
<lastCalibration null="true" />
<measurement>
<unit>Percent</unit>
<value>60</value>
</measurement>
<type>Humidity Sensor</type>
</element>
<element>
<isActive>false</isActive>
<lastCalibration>2020-01-19</lastCalibration>
<measurement>
<unit>Lux</unit>
<value>2</value>
</measurement>
<name>Brightness Sensor</name>
</element>
</root>
JSON
83A564747970657254656D70657261747572652053656E736F726F6C61737443616C6962726174696F6E7819323031382D31312D31335432303A32303A33392B30303A30306B6D6561737572656D656E74A26576616C7565181964756E69746743656C73697573686973416374697665F569707265636973696F6EFB3FB999999999999AA464747970656F48756D69646974792053656E736F726F6C61737443616C6962726174696F6EF66B6D6561737572656D656E74A26576616C7565183C64756E69746750657263656E74686973416374697665F5A4646E616D65714272696768746E6573732053656E736F726F6C61737443616C6962726174696F6E7819323032302D30312D31395432303A32303A33352B30303A30306B6D6561737572656D656E74A26576616C75650264756E6974634C7578686973416374697665F4
[
{
"type": "Temperature Sensor",
"lastCalibration": "2018-11-13",
"measurement": {
"value": 25,
"unit": "Celsius"
},
"isActive": true,
"precision": 0.1
},
{
"type": "Humidity Sensor",
"lastCalibration": null,
"measurement": {
"value": 60,
"unit": "Percent"
},
"isActive": true
},
{
"name": "Brightness Sensor",
"lastCalibration": "2020-01-19",
"measurement": {
"value": 2,
"unit": "Lux"
},
"isActive": false
}
]
Notes: It is light-weight compared to XML and human-readable compared to CBOR. You can see the difference in the representation of the same data in JSON, XML, and CBOR.

## Slide 36
JSON Schema
= Describe + Validate
Notes: It is well-established and has a schema langueage called JSON Schema. It can be used to describe and validate JSON data.

## Slide 37: Another JSON Example: Thing Description
Notes: Make sure to use a TD from the version 1.1: https://www.w3.org/TR/wot-thing-description11/
Here, you can see an example of a TD in JSON format. We will go later into the details of how a TD should be structured and understood.

## Slide 38: Another JSON Example: Thing Description
{
"@context": "https://www.w3.org/2022/wot/td/v1.1",
"title": "MyLampThing",
…
"security": "basic_sc",
"base": “https://example.com”,
"properties": {
"status": {
"type": "string",
"forms": [{"href": "/status"}]
}
},
"actions": {…},
"events":{…}
}
Notes: Make sure to use a TD from the version 1.1: https://www.w3.org/TR/wot-thing-description11/ -> description box.
Here, you can see an example of a TD in JSON format. We will go later into the details of how a TD should be structured and understood.

## Slide 39
NEXT VIDEO
WOT
Payloads
and
Headers
JSON
JSON
in
Practice
Notes: In the next video, we will talk about JSON and what it is in detail.